Henrot	12/10/2023
Adrien
M1 CHPS
adrien.henrot@gmail.com

Lab Report :
C Programming and performance measures

Table of Contents :

1- Introduction : p.3

2- Details on the Architecture : p.3

3- Summary Table : p.3

4- C Programming and Other : p.4

5- Performances Measures and Results Analysis : p.5

6- Dotprod Results : p.6

- Flag -O0 for different compilers : p.6

- Flag -O1 for different compilers : p.7

- Flag -O2 for different compilers : p.8

- Flag -O3 for different compilers : p.9

- Flag -Ofast for different compilers : p.10

7- Reduc Results : p.11

- Flag -O0 for different compilers : p.11

- Flag -O1 for different compilers : p.12

- Flag -O2 for different compilers : p.13

- Flag -O3 for different compilers : p.14

- Flag -Ofast for different compilers : p.15

8- Conclusion : p.16

9- Annexes : p.16

1- Introduction :

The goal of this lab was to test the performances of different algorithms and their different compilation optimizations on three different types of matrices operations such as a DGEMM, a dot product and a reduction. With that in mind we had to use benchmarking technics and take care of our computer stability in order to get viable and exact datas. At least it is what was done for the mesured performances with the Debian computer in the following report as Mac OS does not give you the possibility of manipulation the system as you wish (for instance it has no equivalent of the “taskset” command).

2- Details on the architecture :

First of all we had to extract the information about the computer we were working on. For this lab I’ve worked on two different PCs.

The first one I started on is a x86_64 Mac with an Intel i7 CPU with 6 cores and 16 Go of DDR4 Ram. For the cache line it has : 32Ko for L1 instruction cache and 32Ko for the L1 Data cache, 262Ko for the L2 cache and 9473Ko for the L3 cache (the unit were not precised so they were supposed after the one you find on a classical Linux). On this particular computer I did not find a way to fix the CPU frequency nor how to pin a process to a specified computing core, so with that in mind we have to use the given results as a comparison base knowing that they do not have a particularly value for the performance measuring.

After that I started working on a x86_64 Dell Inspiron with an AMD Ryzen 7 CPU with 16 cores and 16 Go of DDR4 Ram. For the cache line it has a 32Ko L1 data cache, a 32Ko L1 instruction cache a 512 L2 cache and finally a 4096Ko (~4Mo) L3 cache. This PC is running Debian 12 so there was no more problem with fixing the CPU frequency, pinning a process on a core or even verifying the stability of the CPU frequency. So the measurements done with this are more accurate than the one done with the Mac and can be taken into consideration.

3- Summary table :

Computer	Mac	Dell Inspiron
OS	Mac OS Ventura	Debian 12
Architechture	x86_64	x86_64
CPU	Intel i7	AMD Ryzen 7
Cores	6	16
Ram	16 Go DDR4	16 Go DDR4
L1 Data Cache	32 Ko	32 Ko
L1 Instruction Cache	32 Ko	32 Ko
L2 Cache	262 Ko	512 Ko
L3 Cache	9437 Ko (~9.4 Mo)	4096Ko (~4Mo)

4- C Programming and other :

For the C programming part there was no particular difficulties, we had to implement for each operation types an algorithm called unroll eight, the aim of which is to fully load the pipeline. To do so instead of doing multiple loop iteration with one operation each, we divide the number of iteration by eight and we do eight operations at a time. Then if the number of iteration cannot be divided in blocs of eight you have a second loop which ultimately compute the remaining operations.

Then we had to work with GNUplot and that was more difficult as the documentation is not really accessible/well done. The following plots are not necessarily the prettiest ones but they are functional and they show the wanted information. The script used to make them is given as a “plot.p” file for each operation type (it actually is the same script).

Finally we had at some point to modify the given Makefile to test different type of optimization flags and several compiler (such as gcc and clang). In order to do it you can directly change the arguments of the Makefile in the shell with a simple command, instead of juste writing make you can write “make CC=gcc OFLAGS=-O3” for instance to compile the program with gcc and O3 as a flag. For this lab I worked with clang (mac and debian versions) and gcc.
Compiler version	gcc	clang
Mac OS	-	11.0.3
Debian 12	12.2.0	14.0.6

5- Performances Measures and Results Analysis :

In this chapter we had to get the performances measures and analyze them, in order to do so the computer needs to be stable. For the tests done on the Mac I was unable to verify this but I did what I could to assure some sort of stability. Indeed every application was closed, WiFi was off and it was connected to mains power.

For the Dell on the opposite I was able to do so with the use of the “cpupower-frequency-info” Linux command which let the user sets the frequency of the CPU or the governor mode. In my case I used the governor interface to fix it. With the components I have the maximum frequency that can be settled is 1.80 GHz and that corresponds to the performance mode of the governor. So I fixed these values for CPU 1 and then used this CPU to pin the process to perform the different Benchmarks.

Before diving into the results I might as well explain briefly the differences of -O0 to -Ofast optimizations :

- So -O0 means no optimization, it is how you program is normally compiled if you do not specify anything, but it reduces compilation time. It is generally really under-performing for performances.

- Then we have -O1 flag which is the most basic optimization level, the compiler will just try to produce faster and “smaller” code without taking to much compilation time.

- The next one is -O2, it generally is a recommended level of optimization, it has the same flags activated than -O1 but a few more on top. SSE (Streaming SIMD Extension) and AVX (Advanced Vector Extension) might be used at this level. It attempt to increase code performance without compromising on size and without taking to long to compile.

- With -O3 optimization level you have the benefits of the -O2 flag with few expensive optimization on compile time and memory usage. It enables the -ftree-vectorize flag so that loops in our code are getting vectorized and will use AVX YMM registers.

- And finally we have -Ofast which consists of -O3 with -ffast-math and other flags to be really fast but it looses numerical precision in the end.

6- DOTPROD RESULTS :

Flag -O0 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	32211.179	1597.146	2451.492	1740.660	9.139	2629.829
Mac gcc	Unroll 8	9.375	0.009	0	600	500	27157.129	1257.244	1623.340	1475.261	8.426	3102.934
Debian / clang	Base	9.375	0.009	0	600	500	23075.926	1513.278	2949.470	1563.257	15.933	2928.268
Debian / clang	Unroll 8	9.375	0.009	0	600	500	47703.039	1515.340	1530.430	1518.920	0.280	3013.745
Debian gcc	Base	9.375	0.009	0	600	500	48603.146	1513.058	2967.282	1560.838	16.178	2932.808
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	42034.874	1512.254	1533.796	1514.797	0.302	3021.947

Graph :

Observations :

On this first graph we can see that the mac versions are not really coherent with what we can observe about clang and gcc versions. This is probably based on the fact that the computer wasn’t stable. Except that we see that gcc and clang versions seems to have more or less the same performances (and even the same error margin if we refer to the table above). This can be explained thanks to -O0 flag which does not make any optimization.

Flag -O1 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	46161.550	769.156	1032.232	802.411	6.499	5704.856
Mac gcc	Unroll 8	9.375	0.009	0	600	500	48195.433	745.682	776.394	1475.261	2.521	5896.020
Debian / clang	Base	9.375	0.009	0	600	500	60029.575	403.096	1257.718	462.408	41.732	9899.567
Debian / clang	Unroll 8	9.375	0.009	0	600	500	29612.187	392.756	402.334	393.250	0.488	11640.52
Debian gcc	Base	9.375	0.009	0	600	500	97656.747	403.778	1255.152	434.835	34.197	10527.30
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	19591.888	393.436	400.252	393.799	0.355	11624.29

Graph :

Observations :

On this graph we can still see that mac performances are totally out. For the rest of the report we will just take that as granted. On the other hand we can see that here we got some differences between gcc and clang optimizations on the Base algorithm, gcc computes it slightly faster 9899 MiB/s for clang vs 10527 for gcc and the error margin is higher for clang to, 41% vs 34% for gcc. On the unroll algorithm they both perform almost the same but gcc is still better in term of error.

Flag -O2 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	18514.750	769.204	842.934	779.613	2.408	5871.682
Mac gcc	Unroll 8	9.375	0.009	0	600	500	46178.256	738.466	925.740	768.483	4.784	5956.722
Debian / clang	Base	9.375	0.009	0	600	500	28883.707	393.436	499.636	397.788	4.629	11507.72
Debian / clang	Unroll 8	9.375	0.009	0	600	500	133828.076	392.756	400.772	393.721	0.621	11626.59
Debian gcc	Base	9.375	0.009	0	600	500	19357.162	403.096	1193.438	427.948	32.118	10696.71
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	25446.147	392.756	401.372	393.616	0.508	11629.71

Graph :

Observations :

Here things are changing a bit, clang is starting to perform better than gcc on the Base algorithm and is doing way less error, where gcc as a 32% standard deviation we only have 4.6% on clang. So for -O2 on the base algorithm we can say that clang does a better job in order to optimize and vectorize the code. On the other hand they bot perform equally on the Unroll 8 one, “errors” are inferior to 1% and they run at equal speeds.

Flag -O3 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	15535.367	770.602	884.672	780.901	3.110	5861.996
Mac gcc	Unroll 8	9.375	0.009	0	600	500	143525.400	745.316	865.640	776.867	3.013	5892.432
Debian / clang	Base	9.375	0.009	0	600	500	43474.420	393.436	859.752	408.678	19.825	11201.09
Debian / clang	Unroll 8	9.375	0.009	0	600	500	25567.225	392.756	400.190	393.376	0.474	11636.78
Debian gcc	Base	9.375	0.009	0	600	500	26604.832	392.776	1253.690	421.753	35.484	10853.84
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	24961.061	392.756	401.754	394.107	0.718	11615.21

Graph :

Observations :

The same phenomenon as -O2 happens here, gcc is under-performing on the Base algorithm and is doing way more errors. To be able to interpret correctly these results and understand what’s really going on we could take a look at the assembly versions that the compilers are generating. Again for an Unroll type of algorithm they both perform almost equally here clang is still slightly faster and more accurate.

Flag -Ofast for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Debian / clang	Base	9.375	0.009	0	600	500	21585.813	99.766	311.746	162.565	59.350	28158.73
Debian / clang	Unroll 8	9.375	0.009	0	600	500	48015.202	140.764	184.286	143.277	5.231	31949.64
Debian gcc	Base	9.375	0.009	0	600	500	26923.291	198.130	615.614	259.139	53.700	17664.77
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	49945.976	253.254	261.050	254.163	0.873	18010.66

Graph :

Observations :

This is a result that I found funny to add, we can see that for -Ofast gcc is not really that fast compared to it’s -O3 version (only 4k MiB/s more) and does not loose that much accuracy on the unroll algorithm. Whereas on the Base algorithm it gained 20% of standard deviation. Clang for it’s part is indeed much faster than it’s -O3 version but multiplies by 3 it’s standard deviation for the Base algorithm and by ten for then Unroll one. So gcc seems a bit more stable in term of accuracy but is way slower.

7- REDUC RESULTS :

Flag -O0 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	32211.179	1597.146	2451.492	1740.660	9.139	2629.829
Mac gcc	Unroll 8	9.375	0.009	0	600	500	27157.129	1257.244	1623.340	1475.261	8.426	3102.934
Debian / clang	Base	9.375	0.009	0	600	500	23075.926	1513.278	2949.470	1563.257	15.933	2928.268
Debian / clang	Unroll 8	9.375	0.009	0	600	500	47703.039	1515.340	1530.430	1518.920	0.280	3013.745
Debian gcc	Base	9.375	0.009	0	600	500	48603.146	1513.058	2967.282	1560.838	16.178	2932.808
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	42034.874	1512.254	1533.796	1514.797	0.302	3021.947

Graph :

Observations :

Here we start on a new type of algorithm but we have the same sort of results (thankfully). Gcc is still under-performing on the base algorithm for -O0. Just like the results for the dotprod we can see that both compilers are equally accurate. Mac is still totally off in the results.

Flag -O1 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	46161.550	769.156	1032.232	802.411	6.499	5704.856
Mac gcc	Unroll 8	9.375	0.009	0	600	500	48195.433	745.682	861.148	776.394	2.521	5896.020
Debian / clang	Base	9.375	0.009	0	600	500	60029.575	403.096	1257.718	462.408	41.732	9899.567
Debian / clang	Unroll 8	9.375	0.009	0	600	500	29612.187	392.756	402.334	393.250	0.488	11640.52
Debian gcc	Base	9.375	0.009	0	600	500	97656.747	403.778	1255.152	434.835	34.197	10527.30
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	19591.888	393.436	400.252	393.799	0.355	11624.29

Graph :

Observations :

Here we still have coherent results if we compare to the one on the dotprod. Gcc is not that good for the Base algorithm but is doing less errors than clang. And the still perfom equally when it comes to unrolling.

Flag -O2 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	18514.750	769.204	842.934	779.613	2.408	5871.682
Mac gcc	Unroll 8	9.375	0.009	0	600	500	46178.256	738.466	925.740	768.483	4.784	5956.722
Debian / clang	Base	9.375	0.009	0	600	500	28883.707	393.436	499.636	397.788	4.629	11507.72
Debian / clang	Unroll 8	9.375	0.009	0	600	500	133828.076	392.756	400.772	393.721	0.621	11626.59
Debian gcc	Base	9.375	0.009	0	600	500	19357.162	403.096	1193.438	427.948	32.118	10696.71
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	25446.147	392.756	401.372	393.616	0.508	11629.71

Graph :

Observations :

Surprisingly with -O2 gcc is performing well on the base algorithm but when we look in details we find something even more surprising : it’s not accurate at all for this level of optimization. Clang seems to be way more stable globally for now. They still perform equally for Unrolling.

Flag -O3 for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Mac gcc	Base	9.375	0.009	0	600	500	15535.367	770.602	884.672	780.901	3.110	5861.996
Mac gcc	Unroll 8	9.375	0.009	0	600	500	143525.400	745.316	865.640	776.867	3.013	5892.432
Debian / clang	Base	9.375	0.009	0	600	500	43474.420	393.436	859.752	408.678	19.825	11201.09
Debian / clang	Unroll 8	9.375	0.009	0	600	500	25567.225	392.756	400.190	393.376	0.474	11636.78
Debian gcc	Base	9.375	0.009	0	600	500	26604.832	392.776	1253.690	421.753	35.484	10853.84
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	24961.061	392.756	401.754	394.107	0.718	11615.21

Graph :

Observations :

We can observe the exact same thing as for -O2 in terms of performances. Clang is catching up with gcc in term of errors, it has for times the standard deviation it had for -O2. On the other hand gcc is almost equivalent to it’s -O2 version.

Flag -Ofast for different compilers : (programm is running on DRAM)

PC	title	KiB	MiB	GiB	n	r	d	min	max	Mean	Stddev (%)	MiB/s
Debian / clang	Base	9.375	0.009	0	600	500	21585.813	99.766	311.746	162.565	59.350	28158.73
Debian / clang	Unroll 8	9.375	0.009	0	600	500	48015.202	140.764	184.286	143.277	5.231	31949.64
Debian gcc	Base	9.375	0.009	0	600	500	26923.291	198.130	615.614	259.139	53.700	17664.77
Debian / gcc	Unroll 8	9.375	0.009	0	600	500	49945.976	253.254	261.050	254.163	0.873	18010.66

Graph :

Observations :

Here we have still clang performing way better than gcc on the Base algorithm for almost the same error margin but gcc works better and is quit accurate at unrolling under -Ofast.

8- Conclusion :

For every result we got here we have observed that gcc is generally less efficient when it comes to optimizing the Base algorithm and after -O2 flag it’s accuracy become really messed up. It does on the other hand perform better than clang with the -Ofast flag in term of accuracy (not by much but it’s still something to be noted). For -O0 and -O1 the results do not differ that much from one compiler to the other. From -O2 things start to go in two different ways, gcc compile code is having a better accuracy when it comes to unrolling code and keep the same sort of performance than the clang one. Then for -O3 things shifts, gcc compiled code is less accurate than the clang one but no by much (both are under 1% of standard deviation) and they actually keep the same performances. To conclude I think that what we can say after these observations is that clang is good when it comes to optimizing simple algorithms (such as the base one for reduction and dot product) and gcc is better at optimizing unrolling sort of algorithms and is pretty consistent in term of performance and accuracy for those one.

9- Annexes :

Results of benchmarks and plots for DGEMM :
TD2/dgemm/Results/…

Results of benchmarks and plots for dotprod :
TD2/dotprod/Results/…

Results of benchmarks and plots forreduc :
TD2/reduc/Results/...